## Slide 1: Optimizing and Interpreting Deep Learning for IoT Security: An Explainable AI (XAI)Framework for Bi-LSTM-Based Intrusion Detection
Mursaline Huqe
ID : 0242220005101804
Department : CSE
Daffodil International University

## Slide 2: Outline
Introduction
Objective
Background Study
Gap Analysis
Methodology
Results & Analysis
Novelty of the Work
Conclusion
References

## Slide 3: Introduction
IoT now powers homes, industry, and critical infrastructure, but every connected device is a potential entry point for cyber attacks.
Common threats include Mirai botnets, DoS floods, port scans, and MITM ARP spoofing on the IoTID20 benchmark Dataset.
Deep-learning intrusion detection at the edge faces three challenges: large model size, black-box opacity, and adversarial evasion.
This project proposes a lightweight Attention-BiLSTM framework, compressing 69 features to 15 (78.3% reduction) for real-time detection.
Adversarial (PGD-10) training and SHAP explainability add robustness and turn alerts into trustworthy forensic insights.

## Slide 4: Objective
Feature Selection & Compression: Condense 69-dimensional telemetry to a 15-feature subspace, balancing ultra-low latency with multi-class accuracy.
Class-Balanced Permutation Importance inverse-frequency (macro-F1) weighting recovers rare-attack features (e.g. MITM ARP <2%)
CREA projection preserves physical network meaning → 1.49 MB footprint, <0.04 ms/sample inference
Attention-Bi-LSTM : Train a Bidirectional LSTM with dot-product Self-Attention for 5-class detection (Normal, Mirai, DoS, Scan, MITM) on IoTID20.
Target <2.0 MB parameter footprint deployable on low-cost IoT gateways
Real-time inference at <0.04 ms mean latency per sample
Adversarial Evasion Hardening: Apply a Madry minimax attacker-defender loop to harden decision boundaries against FGSM/PGD white-box evasion.
50% of each training batch to convert brittle statistical cues into robust structural patterns
Optimizes the accuracy-robustness trade-off to preserve clean-data performance
Explainable AI (XAI) for Security Forensics: Integrate the SHAP KernelExplainer to turn black-box alerts into analyst-ready forensic evidence.
Global beeswarm plots : feature distributions driving each threat class
Local waterfall charts : packet-level attribution delivered with real-time alerts

## Slide 5: Background Study
Ref. | Authors (Year) | Methodology | Performance Summary | Limitation / Technical Gaps
[1] | Ullah & Mahmoud (2020) | Physical smart-home testbed utilizing the MQTT protocol to generate an IoT benchmark. | Generated the IoTID20 benchmark dataset containing 625,783 records with 83 network features. | Dataset generation only; fails to propose a deep sequence model or establish a <2MB edge gateway baseline.
[9] | Islam et al. (2021) | Bidirectional LSTM (Bi-LSTM) trained on 69 features of the IoTID20 dataset. | Achieved 99.996% binary accuracy on IoTID20; resulted in a 4.26 MB model size footprint. | Fails to meet <2MB edge gateway constraints (4.26 MB); lacks adversarial PGD-10 hardening and XAI transparency.
[17] | Al-Shibly et al. (2026) | Hybrid CNN-BiLSTM with Permutation Importance (PI) feature selection on CIC IIoT 2025. | Reduced feature space to K=20; achieved 0.9720 accuracy and 0.9719 F1-score. | Lacks adversarial PGD-10 hardening (susceptible to gradient-based evasion); does not apply SHAP for packet-level forensic explanation.
[2] | Akintade et al. (2023) | XGBoost with Permutation Importance (PI) alongside SHAP/LIME on NSL-KDD and CCID-V1. | Reduced NSL-KDD features from 42 to 20; achieved 0.8751 AUC in 4.49 seconds runtime. | Applies SHAP only to shallow trees (XGBoost), not deep sequence models; lacks adversarial evaluation.

## Slide 6: Background Study (Cont.)
Ref. | Authors (Year) | Methodology | Performance Summary | Limitation / Technical Gaps
[36] | Sadhwani et al. (2025) | Hybrid BiLSTM-CNN for spatial-temporal extraction over the UNSW-NB15 dataset. | Achieved 97.51% accuracy, 99.265% precision, 93.091% F1-score, and 8.857% Miscalculation Rate. | Lacks adversarial PGD-10 hardening; no SHAP explainability layer for alert validation.
[6] | Madry et al. (2018) | Projected Gradient Descent (PGD) minimax adversarial training framework. | Defines adversarial robustness against L∞ norm ball perturbations at ε=0.05. | Purely mathematical robustness optimization; fails to address <2MB edge gateway constraints or post-hoc SHAP explainability.
[34] | Tsipras et al. (2019) | Mathematical formulation of the accuracy-robustness tradeoff under adversarial training. | Proves a mandatory 4% to 8% standard classification accuracy drop is required for structural defense. | Theoretical framework without empirical IoT deployment, feature compression, or SHAP integration.
[4] | Lundberg & Lee (2017) | SHapley Additive exPlanations (SHAP) framework utilizing KernelExplainer. | Computes unique additive feature attributions for black-box models based on game theory. | General framework; lacks native integration for IoT network packet forensics and adversarial robustness contexts.

## Slide 7: Gap Analysis
None of the reviewed NIDS satisfy all three edge requirements simultaneously:
Memory constraint: uncompressed Bi-LSTMs exceed 4 MB over the <2 MB edge-gateway.
Interpretability loss: PCA-style reduction destroys feature semantics, blocking SHAP forensic explanation.
Adversarial fragility: without PGD-10 hardening, accuracy collapses under FGSM/PGD gradient evasion.
Requirement | Rule IDS | Standard ML IDS | Unoptimized DL IDS | Explainable NIDS | Proposed Framework
Zero-Day Detection | No | Moderate | Yes | Yes | Yes
Edge Footprint (<2.0 MB) | Yes | Yes | No (4.26 MB) | No (3.63 MB) | Yes (1.49 MB)
Adversarial Hardening | N/A | None | None | None | PGD-10 (75.36%)
Local SHAP Explanations | No | No | No | Yes | Yes
Semantic Interpretability | High | High | Low | Low (PCA) | High (PI+CREA)

## Slide 8: Methodology
Preprocessing: drops leakage columns (Cat, Sub_Cat), keeps a stratified 80/20 split, and MinMax-scales to one range, applying SMOTE to the training split only so rare attacks (MITM ARP < 2%) become learnable without leaking into the test set.
Feature selection: an XGBoost surrogate with inverse-frequency class weights scores all 69 features by the macro-F1 drop when each is shuffled, narrowing them to the 15 that carry real multi-class signal from pareto k subsets.
CREA alignment: sweeps k from 1 to 69 to the Kneedle inflection, compresses to 15 features while eigenspace alignment keeps their physical network meaning, then reshapes into a sequence tensor readable later, unlike PCA.
Attention-BiLSTM: reads each flow forward and backward with 64-unit LSTMs, lets Luong self-attention weight the packets that mark an attack, and closes with dropout and a 5-class softmax under a 2 MB footprint.
Adversarial hardening: Madry PGD-10 minimax training perturbs half of every batch (budget 0.05, step 0.0125, 10 steps) to rebuild decision boundaries against white-box evasion, trading a little clean accuracy for real resistance.
SHAP explanation: a KernelExplainer over a 100-sample background ships each alert with the exact features that triggered it a global beeswarm and a per-alert waterfall giving analysts evidence instead of a black-box verdict.

## Slide 9: Dataset & Preprocessing
IoTID20 Dataset
Source: real smart-home testbed (Univ. of Ontario) , SKT NUGU AI speaker and EZVIZ Wi-Fi camera behind an Orange Pi gateway running MQTT, with flows extracted using CICFlowMeter.
Scale: 625,783 flow records described by 83 numerical features plus 3 metadata columns.
Attack types: Mirai botnet, Denial of Service, Scan, and MITM ARP spoofing set against benign traffic.
Class distribution: Mirai 66%, DoS 15%, Normal 15%, Scan 4%, and MITM ARP spoofing < 2% a severely imbalanced mix.
Preprocessing
Stratified split: an 80/20 train-test split (500,332 train / 125,083 test) that preserves the original class ratios.
MinMax scaling: features normalized strictly to [0, 1], fitting the scaler on the training split only to prevent data leakage.
SMOTE oversampling: synthetic oversampling (k = 5 neighbors) on the training split only, lifting the minority MITM ARP class from < 2% toward the majority; the test split is never oversampled.

## Slide 10: Result and Analysis
Class-Balanced Permutation Importance scores for all 69 IoTID20 features, sorted by macro-averaged feature importance.
Rank | Feature | PI Score | Rank | Feature | PI Score
1 | Flow_Duration | 0.3204 | 11 | Pkt_Len_Mean | 0.0017
2 | Src_Port | 0.2708 | 12 | Fwd_Header_Len | 0.0010
3 | Dst_Port | 0.1258 | 13 | Pkt_Size_Avg | 0.0009
4 | Init_Bwd_Win_Byts | 0.0488 | 14 | Idle_Mean | 0.0008
5 | Flow_Pkts/s | 0.0221 | 15 | ACK_Flag_Cnt | 0.0008
6 | Protocol | 0.0103 | 16 | Flow_IAT_Std | 0.0007
7 | Flow_IAT_Max | 0.0085 | 17 | Idle_Max | 0.0006
8 | Flow_IAT_Mean | 0.0048 | 18 | Bwd_Pkt_Len_Std | 0.0006
9 | Flow_IAT_Min | 0.0045 | 19 | Pkt_Len_Max | 0.0006
10 | Bwd_Header_Len | 0.0033 | 20 | Fwd_IAT_Std | 0.0005

## Slide 11: Result and Analysis
Feature Selection & k-Discovery
Class-balanced ranking: applying PI scored all 69 features with an XGBoost surrogate using inverse class-frequency weights, protecting rare attacks such as MITM.
Sequential validation: pareto swept candidate subsets (k = 4, 15, 18, 34, 69) through the full Bi-LSTM to test real sequence-learning ability, not just surrogate scores.
The discovery: k = 18 peaked in the shallow surrogate but collapsed under deep sequential modeling, so k = 15 stands as the optimal subset.
Candidate (k) | Mathematical Criterion | XGBoost Surrogate Harmonic Score | Bi-LSTM Accuracy | Bi-LSTM F1-Macro | Bi-LSTM F1-Worst (MITM) | Bi-LSTM Harmonic Score | Status / Decision
k = 4 | Knee Inflection (Pareto) | 0.7369 | 92.13% | 0.8951 | 0.6433 | 0.5759 | Rejected (Underfitting)
k = 15 | Optimal Inflection Point | 0.7449 | 94.00% | 0.9152 | 0.6996 | 0.6402 | SELECTED
k = 18 | Peak Surrogate Score | 0.7607 | 92.17% | 0.8958 | 0.6329 | 0.5670 | Rejected (Sequence Collapse)
k = 34 | Peak Surrogate F1-Macro | 0.7401 | 93.40% | 0.9098 | 0.6899 | 0.6277 | Rejected (High Footprint)
k = 69 | Full Feature Baseline | 0.7428 | 93.53% | 0.9098 | 0.6891 | 0.6269 | Rejected (Too Complex)

## Slide 12: Result and Analysis
Feature Selection: PI Optimal Subset (k = 15: 69 → 15 features = 78.3% compression)
Rank | Feature Name | Description | Category
1 | Flow_Duration | Total duration of the network flow in microseconds | Temporal
2 | Src_Port | Source port number identifying the origin application | Network
3 | Dst_Port | Destination port number identifying the target application | Network
4 | Init_Bwd_Win_Byts | Number of bytes sent in the initial backward TCP window | Size
5 | Flow_Pkts/s | Number of packets transmitted per second | Rate
6 | Protocol | Transport layer protocol (e.g., TCP, UDP) | Network
7 | Flow_IAT_Max | Maximum inter-arrival time between two packets | Temporal
8 | Flow_IAT_Mean | Mean inter-arrival time between consecutive packets | Temporal
9 | Flow_IAT_Min | Minimum inter-arrival time between two packets | Temporal
10 | Bwd_Header_Len | Total header byte length in the backward direction | Size
11 | Pkt_Len_Mean | Average byte length of packets in the flow | Size
12 | Fwd_Header_Len | Total header byte length in the forward direction | Size
13 | Pkt_Size_Avg | Average size of the packets across the entire flow | Size
14 | Idle_Mean | Average time the flow was idle before becoming active | Temporal
15 | ACK_Flag_Cnt | Number of packets with the Acknowledgment flag set | Flag
Accuracy and macro-F1 comparison for feature subsets k in [4, 15, 18, 34, 69] across evaluated architectures.

## Slide 13: Result and Analysis
Classification: Regular Bi-LSTM (69 feat) vs. Optimized PI + CREA (15 feat)
Binary Classification
Metric | Regular Bi-LSTM (69) | Optimized PI+CREA (15) | Change
Features | 69 | 15 | -78.3%
Accuracy | 99.64% | 99.81% | +0.17%
Precision | 0.9982 | 0.9988 | +0.0006
Recall | 0.9979 | 0.9992 | +0.0013
F1-Score | 0.9981 | 0.9990 | +0.0009
Parameters | 367,233 | 311,937 | -15.1%
Model Size | 4.26 MB | 3.63 MB | -14.8%
Latency | 0.0263 ms | 0.0247 ms | -6.1%
Multi-Class Classification
Metric | Regular Bi-LSTM (69) | Optimized PI+CREA (15) | Change
Features | 69 | 15 | -78.3%
Accuracy | 89.44% | 92.80% | +3.36%
Precision (Macro) | 0.8194 | 0.8765 | +0.0571
Recall (Macro) | 0.9079 | 0.9654 | +0.0575
F1-Macro | 0.8506 | 0.9032 | +0.0526
F1-Worst (MITM) | 0.5267 | 0.6521 | +0.1254
Parameters | 367,749 | 312,453 | -15.0%
Model Size | 4.26 MB | 3.63 MB | -14.8%
Latency | 0.0305 ms | 0.0265 ms | -13.1%
Class-weighted PI preserved the rare MITM ARP class (<2% of data), lifting its F1 by +0.1254.

## Slide 14: Result and Analysis
Adversarial Robustness — Architecture Ablation & PGD-10 Defense
Architectural Ablation (PI + CREA, k = 15)
Architecture | Accuracy | F1-Macro | F1-Worst (MITM) | Parameters | Model Size | Latency (ms)
Standard LSTM (Unidirectional) | 92.07% | 0.8941 | 0.6355 | 123,461 | 1.45 MB | 0.0222
Standard Bidirectional LSTM | 92.80% | 0.9032 | 0.6521 | 312,453 | 3.63 MB | 0.0265
Attention-BiLSTM (Proposed) | 92.62% | 0.9011 | 0.6456 | 378,245 | 1.49 MB | 0.0357
Attention-BiLSTM is the only architecture meeting both the <2.0 MB edge constraint and Bi-LSTM-level accuracy.
PGD-10 Robustness Summary (ε = 0.05)
Model Variant | Clean Acc | PGD-10 Acc (ε=0.05) | Acc Drop | Robustness Gain
Undefended Attention-BiLSTM | 92.62% | 8.21% | -84.41% | — baseline
FGSM-Trained Attention-BiLSTM | 90.32% | 44.04% | -46.28% | +35.83 pp
PGD-Trained Attention-BiLSTM (Final) | 87.99% | 75.36% | -12.63% | +67.15 pp
A -4.63% clean-accuracy concession delivers +67.15 pp PGD-10 robustness — adversarial training is a security imperative.

## Slide 15: Result and Analysis
Explainable AI — SHAP Kernel Explainer (Transparent Threat Alerts)
SHAP KernelExplainer computes each feature's Shapley contribution over a stratified background of 400 training samples across all 5 classes.
Class-Specific SHAP Signatures
Attack Class | Primary SHAP Signature | Physical Interpretation
Mirai Botnet | Src_Port, Protocol, Dst_Port | Algorithmic scanning of specific vulnerable destination ports (e.g., Telnet) over targeted protocols for C2 propagation.
Denial of Service | Src_Port, Protocol, ACK_Flag_Cnt | High-volume protocol exploitation using spoofed source ports and manipulated ACK flags to overwhelm target sensors.
MITM ARP Spoofing | Src_Port, Dst_Port, Protocol | Forged localized routing packets bypassing standard application port mapping to intercept subnet traffic.
Scan / Port Sweep | Src_Port, Dst_Port, ACK_Flag_Cnt | Rapid, sequential reconnaissance pinging across multiple destination network ports, generating abnormal ACK flag responses.
Normal Traffic | Dst_Port, Src_Port, Pkt_Size_Avg | Standard, expected routing ports with regular packet size distributions representing normal browsing communication.

## Slide 16: Result and Analysis

## Slide 17: Novelty of the Work
Simultaneous 3-Way Optimization: First network intrusion detection system (NIDS) to achieve edge-optimized memory footprint (1.49 MB), white-box adversarial hardening (75.36% accuracy under PGD-10 attack), and post-hoc local explainability concurrently.
Interpretability-Preserving Feature Alignment (PI + CREA): Standard PCA creates abstract eigenvectors that make local feature attributions uninterpretable to analysts. Our proposed Constant Rate Eigenspace Alignment (CREA) projects 15 features to an aligned space, gaining +2.45% accuracy over simple selection while keeping 100% human-interpretable feature meaning.
Compressed Attention-BiLSTM Architecture: Eliminates large parameter counts (under 378K parameters) by combining a bidirectional LSTM with a custom Luong self-attention layer. Achieves 92.62% multi-class accuracy at a latency of 0.0357 ms per packet.

## Slide 18: Conclusion
Purpose-built pipeline: An edge-optimized, robust, and explainable deep-learning pipeline for multi-class IoT intrusion detection, delivering three tiers of engineering achievement.
Compression & accuracy: Class-Balanced Permutation Importance with CREA cut 69→15 features (78.3% reduction) on IoTID20, lifting the Bi-LSTM to 99.81% binary and 92.80% multi-class (from 4.26 MB to 3.63 MB); the proposed Attention-BiLSTM reaches 92.62% multi-class in just 1.49 MB at 0.0368 ms per packet.
Adversarial robustness: Under white-box PGD-10 (ε=0.05) clean accuracy collapsed to 8.21%; PGD-10 adversarial training restored it to 75.36% (+67.15 pp) for only a 4.63% clean-accuracy cost (92.62%→87.99%).
Explainability: SHAP KernelExplainer provides a global feature-importance ranking plus local packet-level waterfall plots, making alerts transparent, actionable, and verifiable for security analysts.
Limitations
Accuracy-robustness trade-off: Adversarial training reduces clean accuracy by 4.63% (92.62%→87.99%).
Explanation latency: SHAP KernelExplainer is computationally expensive (𝒪(2ⁿ·T f), computed per class), so local waterfall plots run asynchronously on centralized security hubs rather than in real time on the edge.

## Slide 19: References
[1] I. Ullah and Q. H. Mahmoud, "A Scheme for Generating a Dataset for Anomalous Activity Detection in IoT Networks," in Advances in Artificial Intelligence, Canadian AI 2020, LNCS, vol. 12109, Springer, 2020, pp. 508-520.
[2] S. Akintade, S. Kim, and K. Roy, "Explaining Machine Learning-Based Feature Selection of IDS for IoT and CPS Devices," in 19th IFIP International Conference on Artificial Intelligence Applications and Innovations (AIAI), Springer, 2023.
[3] T. B. Ogunseyi and P. Thiyagarajan, "An Explainable LSTM-Based Intrusion Detection System Optimized by Firefly Algorithm for IoT Networks," Sensors, 2025.
[4] S. M. Lundberg and S.-I. Lee, "A Unified Approach to Interpreting Model Predictions," in Advances in NeurIPS, vol. 30, 2017, pp. 4768-4777.
[5] I. J. Goodfellow, J. Shlens, and C. Szegedy, "Explaining and Harnessing Adversarial Examples," in ICLR, 2015.
[6] A. Madry, A. Makelov, L. Schmidt, D. Tsipras, and A. Vladu, "Towards Deep Learning Models Resistant to Adversarial Attacks," in ICLR, 2018.
[7] N. V. Chawla, K. W. Bowyer, L. O. Hall, and W. P. Kegelmeyer, "SMOTE: Synthetic Minority Over-sampling Technique," JAIR, vol. 16, 2002, pp. 321-357.
[8] T. Chen and C. Guestrin, "XGBoost: A Scalable Tree Boosting System," in KDD '16, 2016, pp. 785-794.
[9] M. N. Islam et al., "Towards Machine Learning Based Intrusion Detection in IoT Networks," CMC, vol. 69, no. 2, 2021, pp. 1801-1821.
[10] S. Hochreiter and J. Schmidhuber, "Long Short-Term Memory," Neural Computation, vol. 9, no. 8, 1997, pp. 1735-1780.
[11] M. Schuster and K. K. Paliwal, "Bidirectional Recurrent Neural Networks," IEEE Trans. Signal Processing, vol. 45, no. 11, 1997, pp. 2673-2681.
[12] X. Chen, M. Liu, Z. Wang, and Y. Wang, "Explainable Deep Learning-Based Feature Selection and Intrusion Detection Method on the Internet of Things," Sensors, vol. 24, no. 16, 2024, p. 5223.
[13] S. Kalakoti, R. Vaarandi, and H. Bahsi, "Evaluating XAI for Deep Learning-Based NIDS Alert Classification," Sensors, 2025.
[14] M.-T. Luong, H. Pham, and C. D. Manning, "Effective Approaches to Attention-based Neural Machine Translation," in EMNLP, 2015, pp. 1412-1421.
[15] H. Ben Ncir, M. Ben HajKacem, and K. A. Alattas, "Enhancing Intrusion Detection Performance Using Explainable Ensemble Deep Learning," IEEE Access, 2024.

## Slide 20: References
[16] A. Grabowski and S. Xu, "Advancing Cybersecurity Practice: Explainable Machine Learning for Network Intrusion Detection," Journal of Cybersecurity Education, Research and Practice, 2024.
[17] A. Al-Shibly, A. Burgas, and J. Massana, "Interpretable Intrusion Detection for IoT: A CNN-BiLSTM Permutation Importance Framework," Frontiers in Big Data, 2026.
[18] A. Abdelaziz et al., "Enhancing Network Threat Detection with Random Forest-Based NIDS and Permutation Feature Importance," Sensors, 2025.
[19] M. T. Ribeiro, S. Singh, and C. Guestrin, "'Why Should I Trust You?': Explaining the Predictions of Any Classifier," in KDD '16, 2016, pp. 1135-1144.
[20] D. Gaspar, P. Silva, and C. Silva, "Explainable AI for Intrusion Detection Systems: LIME and SHAP Applicability on Multi-Layer Perceptron," IEEE Access, 2024.
[21] S. Hariharan, R. R. R. Robinson, R. R. Prasad, C. Thomas, and N. Balakrishnan, "XAI for intrusion detection system: comparing explanations based on global and local scope," Journal of Computer Virology and Hacking Techniques, vol. 19, 2023, pp. 217–239.
[22] C. Zhang, J. Li, N. Wang, and D. Zhang, "Research on Intrusion Detection Method Based on Transformer and CNN-BiLSTM in Internet of Things," Sensors, vol. 25, no. 9, 2025, p. 2725.
[23] S. Kaushik, A. Bhardwaj, A. Almogren, S. Bharany, A. Altameem, A. U. Rehman, S. Hussen, and H. Hamam, "Robust machine learning based Intrusion detection system using simple statistical techniques in feature selection," Scientific Reports, vol. 15, 2025, p. 3970.
[24] I. T. Jolliffe, Principal Component Analysis, 2nd ed. Springer, 2002.
[25] S. G. K. Patro and K. K. Sahu, "Normalization: A Preprocessing Stage," IARJSET, vol. 2, no. 3, 2015.
[26] R. Kohavi, "A Study of Cross-Validation and Bootstrap for Accuracy Estimation," in IJCAI, vol. 14, no. 2, 1995, pp. 1137-1145.
[27] M. Sokolova and G. Lapalme, "A Systematic Analysis of Performance Measures for Classification Tasks," Information Processing & Management, vol. 45, no. 4, 2009, pp. 427-437.
[28] G. Apruzzese et al., "The Role of Machine Learning in Cybersecurity," Digital Threats, vol. 4, no. 1, 2023, pp. 1–38.
[29] N. Capuano et al., "Explainable AI in CyberSecurity: A Survey," IEEE Access, vol. 10, 2022, pp. 93575–93600.

## Slide 21: References
[30] J. Zhang, X. Zhang, Z. Liu, F. Fu, Y. Jiao, and F. Xu, "A Network Intrusion Detection Model Based on BiLSTM with Multi-Head Attention Mechanism," Electronics, vol. 12, 2023, p. 4170.
[31] V. Z. Mohale and I. C. Obagbuwa, "Evaluating machine learning-based intrusion detection systems with explainable AI: enhancing transparency and interpretability," Frontiers in Computer Science, vol. 7, 2025, p. 1520741.
[32] V. Satopaa et al., "Finding a 'Kneedle' in a Haystack: Detecting Knee Points in System Behavior," in ICDCSW, 2011, pp. 166–171.
[33] M. A. Ferrag et al., "Deep Learning for Cyber Security Intrusion Detection: Approaches, Datasets, and Comparative Study," J. Info. Sec. Applications, vol. 50, 2020, p. 102419.
[34] D. Tsipras, S. Santurkar, L. Engstrom, A. Turner, and A. Madry, "Robustness May Be at Odds with Accuracy," in ICLR, 2019.
[35] M. Shafiq et al., "A Hybrid BiLSTM-CNN Approach for Intrusion Detection for IoT Applications," Electronics, 2024.
[36] S. Sadhwani, A. Navare, A. Mohan, R. Muthalagu, and P. M. Pawar, "IoT-based Intrusion Detection System Using Explainable Multi-class Deep Learning Approaches," Computers and Electrical Engineering, vol. 123, 2025, p. 110256.
[37] N. G. Pour and S. Shemehsavar, "DCB-VIM: An Ensemble Learning Based Filter Method for Feature Selection with Imbalanced Class Distribution," Neurocomputing, vol. 651, 2025, p. 130848.
[38] D. Alomari, M. A. Alabdullatif, and F. A. Khan, "An Explainable AI-based Network Intrusion Detection System for Botnet Attacks," in EASE Companion 2025, 2025, pp. 169-175.
[39] E. W. Sholeha, D. Y. Jaya, and Q. A. Fitroh, "Explainable Machine Learning for Network Intrusion Detection Using SHAP-Based Feature Interpretation," Journal of Information Systems and Informatics, 2024.

## Slide 22
THANK YOU